| Inspected by | W. A. Wong | Date | 11 January 2006 |
| --- | --- | --- | --- |
| Signature |  | Reviewed by | C.C. Wong |

Please tick the appropriate box 0 – serious nonconformity, requires issue of CAR (fill the corrective action request form) 1 – not satisfied, but immediate remedial action was taken and found acceptable 2 - satisfied Important : Please refer to the requirements as defined in EI-03—08 Environmental Instructions

| Items to be checked | 0 | 1 | 2 | N/A | Comment / Follow up |
| --- | --- | --- | --- | --- | --- |
| Waste management |  |  |  |  |  |
| Solid wastes are segregated and collected properly? |  |  | ( |  |  |
| Solid wastes are stored at designated areas with proper labelling and cover? |  |  | ( |  |  |
| Chemical wastes are stored at designated containers and areas? And in good conditions? |  |  | ( |  |  |
| Chemical wastes are properly labelled and closed? |  |  | ( |  |  |
| Waste disposal records are maintained? |  |  | ( |  |  |
| Secondary containment and adequate ventilation for storage areas are provided? |  |  | ( |  |  |
| Air pollution control |  |  |  |  |  |
| Plating baths are properly covered when not in use? |  |  | ( |  |  |
| Ventilation systems / air pollution control systems are properly maintained and in good conditions ? |  |  | ( |  |  |
| No abnormal fume / smell is observed ? |  |  | ( |  |  |
| Effective maintenance of plant and equipment through visual inspection and records review are performed? |  |  | ( |  |  |
| Water pollution control |  |  |  |  |  |
| Wastewater treatment plant is operated properly and in good conditions? |  |  | ( |  |  |
| Wastewater arising from electroplating process is segregated and directed to in-house wastewater treatment plant? |  |  | ( |  |  |
| Wastewater treatment plant is cleaned and maintained regularly and records maintained? |  |  | ( |  |  |
| Noise pollution control |  |  |  |  |  |
| Routine maintenance conducted and records of all inspections and maintenance works maintained? |  |  | ( |  |  |
| No abnormal noise is observed from equipments and operations? |  |  | ( |  |  |
| Resource conservation |  |  |  |  |  |
| No running tap (when they are not in use) or water leakage is observed? |  |  | ( |  |  |
| Switch off electrical appliance when they are not in use ? |  |  | ( |  |  |
| Sufficient drain time provided above the process bath to reduce the quantity of dragout? |  |  | ( |  |  |
| The temperature of plating baths is set properly? |  |  | ( |  |  |
| Handling and storage of chemicals |  |  |  |  |  |
| Drip trays are provided for chemical storage? |  |  | ( |  |  |
| Chemicals are properly labelled and stored in good conditions? |  |  | ( |  |  |
| Chemical spillage kits are maintained properly? |  |  | ( |  |  |
| Mixing areas are well lit and ventilated, and are as close to their point of use as possible? |  |  | ( |  |  |
| Others: |  |  |  |  |  |