Hong Kong Green Electroplating Company

Environmental Instruction Waste Management (EI-03)

Revision No. : 1

Date : 01 – 01 – 2006

| Prepared by : | CC Wong |
| --- | --- |
|  | (EMR) |
| Approved by : | PH Lau |
|  | (General Manager) |

###### Revision History

| Revision Date | Description | Sections Affected | Revised By | Approved By |
| --- | --- | --- | --- | --- |
| 01-01-2006 | First issue | - - | - - | PH Lau |

- Purpose

This instruction outlines the practices to be adopted for waste management and to comply with legal and other requirements.

- Scope

This instruction is applicable to all activities and operations in the company which generates wastes and includes the best practice procedures for managing:

- Solid Waste; and

- Chemical Wastes.

Some solid wastes in which HKGEC produces include:

  - Packaging materials (plastic strips, carton boxes, etc.)

  - General refuse from office activities

  - Metal wastes such as copper, nickel and alloys

  - Recyclable wastes (e.g. paper, plastic bottles, aluminum cans, etc.)

Some chemical wastes in which HKGEC produces include wastes from:

- Degreasing agents and NaOH from degreasing process

- Plating chemicals such as copper, nickel, silver, gold and palladium-nickel salts

- Caustic soda, hydrochloric acid, sulphuric acid and hydrogen peroxide used in wastewater and deionised (DI) water systems

- Paint, acetylene, adhesives, lube oil, hydraulic oil, aerosols, heat transfer oil and organic solvents used in general facility maintenance.

- Empty chemical containers

- Procedure

  - Application for permits/licences

The EMR shall ensure that:

- a chemical waste producer licence is obtained for the company, and that the licence covers all the types of chemical waste produced by the company.

  - Practices for Waste Management

    - General Waste Management

- Segregation

  - Segregate the following solid wastes for disposal or recycling:

- Non-recyclable solid wastes (general refuse, spent filters after cleaning, non-recyclable packaging bags/wraps, etc.)

- Paper wastes for recycling (do not place non-recyclable paper including carbon paper, plastic laminated paper, glossy paper and contaminated papers in the recycle paper container)

- Packaging wastes (cartons, boxes) for recycling

- Wooden pallets for recycling

- Metal wastes (e.g. copper, nickel) for recycling

- Toner cartridges for recycling (return to suppliers)

- Plastic bottles for recycling

- Aluminium cans for recycling

- Bulky items (e.g. furniture, machinery) fluorescent tubes, batteries, for disposal

  - Clearly labelled containers must be located for the initial collection of these wastes as near as conveniently possible to the point of generation.

  - A designated member of staff (usually cleaning staff) should be assigned to collect the wastes and transfer them to the waste storage area regularly.

- Storage

  - Segregate chemical waste and general waste in accordance with the allowable waste types listed on the containers.

  - Store all waste containers in dedicated storage areas.

  - Put lids/covers on all refuse containers.

  - Label all waste containers and waste storage areas.

  - Store all waste containers on sealed ground to avoid land contamination

- Disposal

  - General refuse shall be collected daily by Building Management Office (BMO)’s collector.

  - Return toner cartridges, wooden pallets, metal workpieces to suppliers

  - All recyclable wastes : paper, cartons, plastic bottles, aluminium cans, batteries and fluorescent tubes collected shall be placed to the recycling bins provided by BMO for recycling (collected by BMO’s waste collectors and recyclers)

    - Chemical Wastes Management

- Chemical wastes include :

  - spent acid (from acid dip bath),

  - spent alkali (from degreasing bath)

  - spent metal concentrate (spent plating baths)

  - sludge and spent resin (from wastewater treatment plant)

  - contaminated rags and gloves

  - chemical containers

  - spent lube oil, hydraulic oil, solvent from maintenance works

- Register with Environmental Protection Department (EPD) as Chemical Waste Producer and apply for a revision if the types of chemical waste to be disposed of change.

- Appoint licensed collector(s) (from EPD’s list of approved registered chemical waste collectors) to collect and dispose of chemical wastes

- Maintain records (trip tickets) of chemical wastes generated / collected.

- Adopt alternative working practices / processes to eliminate / reduce / generate less toxic chemical wastes

- Adopt storage, handling, transportation and disposal practices in accordance to the EPD publication “Code of Practice on the Packaging. Labelling and Storage of Chemical Wastes”:

- Provide appropriate wastes containers for each type of chemical waste generated on site. (Use container with capacity less than 450 litre unless specification approved by EPD.)

- Ensure that containers are in good condition, closed/ sealed.

- Put chemical waste labels with the appropriate information (in Chinese and English) on chemical waste containers

- maintain waste containers upright to minimise spillage/leakage.

- Designate separate storage facilities for incompatible chemical waste, and provide these areas with prominent signage, lock, etc.

- Provide secondary containment (e.g. drip trays or impermeable floor and bunding) and adequate ventilation for storage areas. (Capacity of the secondary containment should be able to accommodate 110% of the volume of the largest container or 20% of the total volume of waste stored, whichever is greatest.)

- Provide storage area with impermeable floor and bunding, and adequate ventilation.

- Monitoring and Checking

The EMR shall ensure that:

- waste facilities specified in this EI are provided adequately and operated in satisfactory conditions; and

- Waste management practices specified in this EI are followed by staff and contractors.

The Plant Manager or his / her delegate shall:

- Check weekly if practices in Section 3.2 are correctly and fully implemented by random visual inspection.

- When nonconformity are identified, corrective action measures shall be defined and implemented in accordance with EP-07 Enquiry / Complaint / Nonconformity Handling.

- Records

| Record Description | Record Location/ Retention Responsibility | Minimum Retention Time |
| --- | --- | --- |
| Lists of chemicals wastes and storage locations (Refer to Production Manager) | EMR | Two previous versions |
| Information on waste collection company and frequency of collection locations (Refer to individual trip-ticket records and general waste collection records from subcontractor) | EMR | 3 years |
| MSDS for all chemicals (Refer to Production Manager) | EMR | 3 years |
| Trip Tickets (Refer to Production Manager) | EMR | 3 years |

- Appendix

Nil.