Company Information of Hong Kong Green Printed Circuit Board Company (HKGPCB)

| Company Name | Hong Kong Green Printed Circuit Board Company (HKGPCB) |
| --- | --- |
| Business Nature | Manufacture of multi-layer printed circuit boards (PCB) |
| Products | PCB for computers, telecom equipment, automotive and industrial control |
| Major Markets / Clients | China, Asia, Europe, USA |
| Manufacturing Processes | First Cut / Board Cut ( Inner Dry Film & Etching ( Black Oxide ( Pre-lay / Lay Up ( Pressing ( Second cut ( tooling hole drilling, drilling and laser drilling ( Deburr ( Desmear ( Vertical PTH and Panel plating ( Pattern plating ( Outerlayer etching and tin stripping ( Soldermask ( Surface finishing hot air levelling ( Surface Finishing -- Electroless Nickel Immersion Gold ( Surface Finishing -- Gold Finger Plating / Bondable Gold Plating ( Component mark ( ENTEK (organic coating on copper surface) ( Routing ( Ultrasonic Cleaning ( packing ( delivery |
| Address Office and Plant Locations | 2/F, 3/F., 50 Dai Wang Street, Tai Po Industrial Estate, Tai Po, New Territories, Hong Kong |
| Factory Areas | 2,000 m2 |
| No. of employees | 60 |
| Main facilities / equipment | PCB plating and etching line Board cutting machine Drilling machine Dry room for film developing Boiler Water cooling system D.I. water generating system Wastewater treatment plant Air extraction and pollution control system Air compressors Warehouse Laboratory |
| Surrounding Environment | 2nd and 3rd floors in a multi-storey industrial building located at Tai Po Industrial Estate. Neighbouring factories are metal moulding factory and concrete batching plant. |
| Potential Environmental Impacts from the Operations | Wastewater discharge from etching, electroplating, cleaning, film developing and rinsing processes. Wastewater is discharged to public sewers of Tolo Water Control Zone. Solid wastes include general refuse, papers, packaging bags, metal wastes, spent laminate sheets and rejected products, etc. Chemical wastes from spent plating baths, dry film residues, sludge, spent lubricant oil and chemical containers. Acid / alkaline / metal mists from chemical processing baths, VOC emission from use of solder mask, solvent and chemicals, etc. Noise from board cutting and drilling processes, water pumps, air compressors, etc. Significant use of electricity, water and chemical for production processes. |
| Special Client’s Environmental Requirements | Nil |

Disclaimer : The information provided in this practical example is purely hypothetical and intended to illustrate the development and implementation of ISO 14001 EMS.  Users will need to ensure that the information they insert is appropriate for their own situation.

# Layout Plan – 2/F

Layout plan – 3/F

Process flow

Material Preparation / Baking

Thermal Cured

| Pressing |  | Soldermask Printing |
| --- | --- | --- |

| Oxide Treatment |  | Liquid-Photoimageable Soldermask Printing |
| --- | --- | --- |

| Tooling Hole Drilling / Primary, Secondary X-ray Drilling |  | Dip Cell Gold / Nickel Plating |
| --- | --- | --- |

| Ultrasonic Deburring |  | Electroless Nickel / Immersion Gold |
| --- | --- | --- |

| Desmear /PTH |  | Hot Air Solder Leveling (HASL) |
| --- | --- | --- |

| Diazo Phototool Preparation |  | Routing / Blanking / V-Cutting / Bevelling |
| --- | --- | --- |

| Innerlayer/Outerlayer Dry Film Imaging |  | Final Clean |
| --- | --- | --- |

| Panel Plating |  | Packaging / Delivery |
| --- | --- | --- |

Pattern Plating

Alkaline Etching

### Location Map

2/F, 3/F., 50 Dai Wang Street, Tai Po Industrial Estate, Tai Po, New Territories, Hong Kong

# Text boxes

Production and Engineering Office

Exit

Surface Finishing Hot Air Leveling

Solder Mask Room

Etching & Stripping Line

Pattern Plating Line

Vertical PTH and Panel Plating Line

Deburr & Dismear Room

Block Oxide

Inner Dry Film & Etching

First Cut / Board Cut Room

Pre-lay / Lay up Room

Laser Drilling Room

Drilling Room

Pressing Room

Cutting Room

Boiler

Water Cooling System

Surface Grinding

Dry Room

Component Mark / Entek

Material Storage

Chemical Storage

Packing

Warehouse

D.I. Water System

Wastewater Treatment System

Physical & Chemical Laboratory

Exit

Production / Engineering

Office

General

Office

#### HKGPCB

Metal Moulding factory

Concrete batching plant

Anodizing factory

Metal Surface Finishing factory

#### HKGPCB