HONG KONG ENVIRONMENTAL ELECTRICAL APPLIANCE COMPANY

Environmental Instruction Air Pollution Control (EI-04)

Revision No. : 1

Date : 01 – 01 – 2006

| Prepared by : | Mason Lee |
| --- | --- |
|  | (EMR) |
| Approved by : | Jonathan Ho |
|  | (Managing Director) |

###### Revision History

| Revision Date | Description | Sections Affected | Revised By | Approved By |
| --- | --- | --- | --- | --- |
| 01-01-2006 | First issue | - - | - - | Jonathan Ho |

- Purpose

This instruction outlines the practices to be adopted for the control of air emissions to minimise air pollution impacts and to comply with legal and other requirements.

- Scope

This instruction is applicable to the site activities, which have the potential to cause air pollution, and includes best practice procedures for the following:

- Emission of Offensive / Obnoxious Emissions & Dark Smoke from Plant and Equipment, including:

  - Emission from soldering and oven;

  - Emission from painting process; and

  - VOC emission during assembly process

- Maintenance/control over applicable activities and operations that generate airborne pollutants, including air compressors, soldering and oven.

- Control of Chlorofluorocarbon (CFC) (e.g. refrigerants in air-conditioning units and CFC fire extinguishers).

- Procedure

  - Application for permits / licences

The EMR or his / her delegate shall ensure that approval is sought from Environmental Protection Department for installation or alteration of any furnace, oven, chimney or flue according to APCO - Air Pollution Control (Furnaces, Oven and Chimneys) (Installation and Alteration) Regulation.

  - Best Practices for Air Pollution

    - Emission of Offensive / Obnoxious Emissions & Dark Smoke from Plant and Equipment

- Conduct routine and major maintenance in accordance to manufacturer’s instructions, and maintain records of all inspections and maintenance works.

- Use fuel of quality specified by manufacturer / supplier.

- Perform weekly visual inspections of plants and equipment using Ringlemann chart  by the Production Manager or his / her delegate.

    - Maintenance / control over applicable activities and operations which generate airborne pollutants

- Ensure sufficient ventilation in indoor area especially rooms for chemicals usage and storage.

- Ensure that the air treatment equipments (e.g. air scrubbers, filtering system) function properly through regular inspection and maintenance.

- Clean dust filter regularly for efficient dust control.

    - Management of CFC

- Ensure maintenance contractors carrying out maintenance and repair in accordance with requirements stipulated in the Ozone Layer Protection (Controlled Refrigerants) Regulations

- Switch to A/C units/systems that use non-scheduled refrigerants during replacement.

- Switch to non-CFC fire extinguisher if applicable.

- Monitoring and Checking

The EMR shall ensure that :

- facilities / plant with the potential impact for air are operated and maintained in satisfactory conditions;

- practices specified in this procedure are followed by staff and contractors; and

- the requirements of the APCO are complied with.

The Production Manager or his / her delegate shall:

- ensure the effective maintenance of plant, equipment and vehicles through visual inspection and document / records review

- perform quarterly monitoring on the quality of indoor air and exhausted air.

- where nonconformity are identified corrective action measures are defined and implemented in accordance with EP-07 Enquiry / Complaint / Nonconformity Handling.

- Records

| Record Description | Record Location/ Retention Responsibility | Minimum Retention Time |
| --- | --- | --- |
| Maintenance schedules / records for plant, equipment and vehicles (Refer to relevant subcontractors for plant, equipment and vehicles maintenance record) | Production Manager | 3 years |
| Visual Inspection Records (Refer to EF-EP07-01 if found any nonconformity item) | Production Manager | 3 years |
| Air quality monitoring record (EF-EI04-01) | Production Manager | 3 years |

- Appendix

Appendix 1 : Air Quality Monitoring Record (EF-EI04-01)

| Date | Inspector | Inspection Area | Responsible staff of inspection area | Findings | Remarks |
| --- | --- | --- | --- | --- | --- |

# Footnotes

The smoke produced from the plant/equipment is compared to a Ringlemann chart and if the shade of the smoke is as dark or darker than the shade Number 1 on the Ringlemann Chart for period of 3 minutes, legal requirements for black smoke emissions are violated and the Factory Manager records a nonconformity to the EMS.