HONG KONG ENVIRONMENTAL ELECTRICAL APPLIANCE COMPANY

Environmental Instruction Water Pollution Control (EI-05)

Revision No. : 1

Date : 01 – 01 – 2006

| Prepared by : | Mason Lee |
| --- | --- |
|  | (EMR) |
| Approved by : | Jonathan Ho |
|  | (Managing Director) |

###### Revision History

| Revision Date | Description | Sections Affected | Revised By | Approved By |
| --- | --- | --- | --- | --- |
| 01-01-2006 | First issue | - - | - - | Jonathan Ho |

- Purpose

This instruction outlines the practices to be adopted for water pollution control and to comply with legal and other requirements.

- Scope

This environmental instruction is applicable to the activities and operations which gives rise to water pollution and includes best practice procedures for the following:

- Prevention of contamination of drains/gullies; and

- Wastewater treatment methodology (reused and collected by wastewater treatment collectors);

The major source of wastewater generated from production is the rinsing process during paint spraying and powder coating process.  Some domestic wastewater arises from flushing and pantry in the office.

- Procedure

  - Application for permits/licences

The EMR shall ensure that:

- A wastewater discharge licence is obtained from EPD

- The wastewater treatment methodology specified in the licence are provided and operated in satisfactory conditions; and

- The discharge limits and monitoring requirement specified in the discharge licence complied with.

  - Best Practices for Water Pollution Control

    - Contaminated Drains / Gullies

- locate drip trays underneath equipment for operation, fuelling and maintenance;

- provide secondary containment and roofing for fuel/liquid chemical storage areas;

- use oil interceptors to remove any oil/grease deposits, and dispose of the sludge as chemical waste in accordance to EI-03 for Waste Management;

- adopt waste oil disposal/minor spillage procedures in accordance with EI-03 for Waste Management;

- for emergency spillage and leakage follow measures described in EP-05.

    - Wastewater Treatment Methodology

- Wastewater arising from operation should be segregated, and to be collected and treated by qualified wastewater treatment company

- Engineer has to ensure wastewater treatment contractor to perform the treatment properly and maintain records.

- For emergency situation, resulting in shutdown of equipments, actions taken in accordance with the instruction of wastewater treatment collection provided by the contractor and contacts the contractor immediately for further actions.

- Monitoring and Checking

The EMR shall ensure that:

- facilities specified in this EI are provided adequately;

- practices specified in this EI are followed by staff and relevant contractors; and

- the discharge limits and monitoring requirement specified in the discharge licence are complied with.

The Production Manager or his / her delegate shall:

- ensure that sufficient measures are carried out to control water pollution from company operations and activities.

- employ HOKLAS laboratory on a quarterly basis to sample effluent from each of the external discharge points of the site and perform analysis for parameters specified on the discharge licence. This is to confirm compliance and assessment of the effectiveness of the mitigation measures.

- carry out weekly site inspection of the effectiveness of the water pollution control measures, and note down the observation in the relevant inspection checklists.

- where nonconformity are identified corrective action measures are defined and implemented in accordance with EP-07 Enquiry / Complaint / Nonconformity Handling.

- Records

| Record Description | Record Location/ Retention Responsibility | Minimum Retention Time |
| --- | --- | --- |
| Effluent Monitoring records (Refer to individual effluent point monitoring record) | EMR | 3 years |
| Visual Inspection Records (Refer to EF-EP07-01 if found any nonconformity item) | Production Manager | 3 years |

- Appendix

Nil.