Company Information of Shenzhen Environmental Printed Circuit Board Company (SZEPCB)

| Company Name | Shenzhen Environmental Printed Circuit Board Company (SZEPCB) |
| --- | --- |
| Business Nature | Double and multilayer printed circuit boards |
| Products | Manufacture of PCB for mobile phones |
| Major Markets / Clients | Forward Mobile Group (Asia, Europe, America) |
| Manufacturing Processes | General ( Material Preparation/ Baking ( Pressing ( Oxide Treatment ( Tooling Hole Drilling/ Primary, Secondary X-Ray Drilling ( Ultrasonic Deburring ( Desmear/ PTH ( Diazo Phototool Preparation ( Innerlayer / Outerlayer Dry Film Imaging ( Panel Plating ( Pattern Plating ( Alkaline Etching ( Thermal Cured Soldermask Printing ( Liquid-Photoimageable Soldermask Printing ( Dip Cell Gold/ Nickel Plating ( Electroless Nickel/ Immersion Gold ( Hot Air Solder Leveling (HASL) ( Routing/ Blanking/ V-cutting/ Bevelling ( Final Clean ( Packaging/ Delivery |
| Address Office and Plant Locations | Unit 12, 8/F Block F Yung Fat Building 186-212 Wu Yi Hop Road Kwai Chung NT | G/F, 40 Harbour Road, Shekou Industrial Zone, Shenzhen, Guangdong, PRC 中國深圳經濟特區 蛇口工業區港灣大道 |
| Factory Areas | 115,000m2 |
| No. of employees | HK Office : 8 Shenzhen Factory : 85 |
| Main facilities / equipment | PCB plating and etching line Board cutting machine Drilling machine Dry room for film developing Warehouse Laboratory Boiler Water cooling system D.I. water generating system Wastewater treatment plant Air extraction and pollution control system Oven Dormitory Emergency generator |
| Surrounding Environment | Lower floors in a multi-storey industrial building located at Shekou Industrial Zone in Shenzhen PRC. Neighbour factories are shoe manufacturing factory and a plastic factory. (see site layout attached) |
| Potential Environmental Impacts from the Operations | Wastewater discharge from etching, electroplating, cleaning, film developing and rinsing processes. Wastewater is discharged to the treatment facility in Shekou Industrial Zone. Solid wastes include general refuse, papers, packaging bags, heavy metal and precious metal wastes, spent laminate sheets and rejected products, etc. Chemical wastes from spent plating baths, dry film residues, sludge, spent lubricant oil and chemical containers. Acid / alkaline / metal mists from chemical processing baths, VOC emission from use of solder mask, solvent and chemicals, etc. Noise from mixers, water pumps, and air compressors, etc. Significant use of electricity, water and chemical for production processes. |
| Special customer’s environmental requirements | Forward Mobile Group: comply with environmental regulations properly documented ISO 14001 EMS and/or a plan for its implementation suppliers have to provide raw material contents and end of life treatment recommendations relevant to client’s specifications upon request. |
| Relevant Legislation Related to Client’s Environmental Requirements | For Europe The Restriction of Hazardous Substances in Electrical and Electronic Equipment (ROHS) Directive (2002/95/EC) Nickel Free Directive (Directive 94/27/EC) |

Disclaimer : The information provided in this practical example is purely hypothetical and intended to illustrate the development and implementation of ISO 14001 EMS.  Users will need to ensure that the information they insert is appropriate for their own situation.

# Factory Layout Plan

Process flow

Material Preparation / Baking

Thermal Cured

| Pressing |  | Soldermask Printing |
| --- | --- | --- |

| Oxide Treatment |  | Liquid-Photoimageable Soldermask Printing |
| --- | --- | --- |

| Tooling Hole Drilling / Primary, Secondary X-ray Drilling |  | Dip Cell Gold / Nickel Plating |
| --- | --- | --- |

| Ultrasonic Deburring |  | Electroless Nickel / Immersion Gold |
| --- | --- | --- |

| Desmear /PTH |  | Hot Air Solder Leveling (HASL) |
| --- | --- | --- |

| Diazo Phototool Preparation |  | Routing / Blanking / V-Cutting / Bevelling |
| --- | --- | --- |

| Innerlayer/Outerlayer Dry Film Imaging |  | Final Clean |
| --- | --- | --- |

| Panel Plating |  | Packaging / Delivery |
| --- | --- | --- |

Pattern Plating

Alkaline Etching

Location of Shenzhen Environmental Printed Circuit Board Company (SZEPCB)

# Text boxes

Liquid-Photoimageable Soldermask Printing

Soldermask Printing

Thermal Cured

Alkaline Etching

Pattern Plating

Panel Plating

Innerlayer / Outerlayer Dry Film Imaging

Diazo Phototool Preparation

Exit

Desmear / PTH

Ultrasonic Deburring

Tooling Hole Drilling / Primary, Secondary X-ray Drilling

Oxide Treatment

Pressing

Material preparation / Baking

Dip Cell Gold / Nickel Plating

Electroless Nickel / Immersion Gold

Hot Air Solder Leveling

Routing / Blanking / V-Cutting / Bevelling

Warehouse, Packaging / Delivery

Final Clean

Office

DI water generation plant

Wastewater Treatment Plant

Laboratory

Canteen

Dormitory

Location of Shenzhen Environmental Printed Circuit Board Company (SZEPCB): G/F, 40 Harbour Road,

Shekou Industrial Zone,

Shenzhen