# Annex II

# Proposed Final Water Quality Criteria - Summary

# Environmental and Engineering Feasibility Study (EEFS)

Table 1.	Proposed Water Quality Criteria at Edge of Initial Dilution Zone

| Parameter | Value | Period/Type |
| --- | --- | --- |
| Unionised ammonia | < 0.021 mg/L < 0.035 mg/L < 0.233 mg/L | annual average 4-day average 1-hour average |
| pH | 6.5 – 8.5, and change < 0.2 | at least 90% of occasions |
| Temperature | change < 2℃ | at least 90% of occasions |
| Sulphide | < 0.02 mg/L | at least 90% of occasions |
| Cyanide | < 0.005 mg/L | at least 90% of occasions |
| Total residual chlorine | < 0.013 mg/L | Daily maximum |
| Surfactants | < 0.03 mg/L | at least 90% of occasions |
| Copper | < 0.005 mg/L | at least 90% of occasions |
| Nickel | < 0.005 mg/L | at least 90% of occasions |
| Total chromium | < 0.05 mg/L | at least 90% of occasions |
| Zinc | < 0.02 mg/L | at least 90% of occasions |
| Mercury | <0.00021 mg/L | at least 90% of occasions |
| Arsenic | < 0.02 mg/L | at least 90% of occasions |
| Phenol | < 0.005 mg/L | at least 90% of occasions |
| Acute toxicity | 0.3 acute toxicity units1 (derived from LC50 values based on whole effluent toxicity tests) | One hour average condition not to exceed this value |

1 USEPA Technical Support Document for Water Quality-Based Toxics Control (March 1991), from which one acute Toxicity Unit (TU) is defined as

TU (acute) = 100/LC50, where LC50 = % of effluent which gives 50% survival of the most sensitive of the range of species tested

Table 2.	Additional Water Quality Criteria at Edge of Mixing Zone

| Parameter | Value | Period/Type |
| --- | --- | --- |
| Dissolved oxygen | for W & E Buffer Zones, Junk Bay and Victoria Harbour : > 4 mg/L (water column average), and > 2 mg/L | at least 90% of occasions during the year at all times |
|  | for Southern Waters and waters in other zones that overlap with fish spawning grounds shown in Figure 1: > 5 mg/L (water column average), and > 2mg/L | Average in each month of the year at all times |
| Total inorganic nitrogen | < 0.2 mg/L for Southern Waters and waters in other zones that overlap with fish spawning grounds shown in Figure 1 < 0.4 mg/L for W & E Buffer Zones and Victoria Harbour < 0.3 mg/L for Junk Bay | annual water column average |
| Total inorganic phosphorus | < 1/10 TIN criterion | annual water column average |
| Chronic toxicity | < one chronic toxicity unit (TU), as determined in accordance with USEPA Procedures2 | 4-day average chronic toxicity exposure |
| Total residual chlorine | < 0.008 mg/L | Daily maximum |

2 one chronic toxicity unit is defined as TU (chronic) = 100/NOEC (chronic), where NOEC is the No Observed Effect Concentration, based on the most sensitive of the range of species tested

Table 3.	Additional Water Quality Criteria for Specific Beneficial Uses or Zones

| Parameter | Value | Period/Type | Where Applicable |
| --- | --- | --- | --- |
| E.coli | < 1,800/L < 6,100/L < 200,000/L | Geometric mean Geometric mean > 90% of occasions | Bathing waters Secondary contact recreation and mariculture zones Flushing or industrial use |
| Dissolved oxygen | > 5 mg/L (water column average), and > 2 mg/L (bottom 2 m) | at least 90% of occasions during the year | mariculture zones |
| Total inorganic nitrogen | < 0.1 mg/L | Annual average | Semi-enclosed bays (e.g. Tai Tam Bay, Port Shelter) |