Environmental Impact Assessment Ordinance (Cap. 499)

Section  5 (7)

Environmental Impact Assessment Study Brief  No. ESB-034/1999

Project Title : New World First Bus Permanent Depot at Chai Wan

Name of Applicant : New World First Bus Services Limited

1.	BACKGROUND

1.1	An application (No. ESB-034/1999) for an Environmental Impact Assessment (EIA) study brief under section 5(1) of the Environmental Impact Assessment Ordinance (EIAO) was submitted by the Applicant on 14 June 1999 with a project profile (No. PP-050/1999) .

1.2	The Applicant proposes to provide a permanent depot building for bus parking and maintenance facilities in Chai Wan.  The proposed bus depot is a multi-storey building comprising various provisions to facilitate different repairing and maintenance operation needs as well as for bus parking services.

1.3	Pursuant to section 5(7)(a) of the EIAO, the Director of Environmental Protection (the Director) issues this EIA study brief to the Applicant to carry out an EIA study.

1.4 	The purpose of this EIA study is to provide information on the nature and extent of environmental impacts arising from the construction and operation of the proposed designated project and related activities taking place concurrently.  This information will contribute to decisions by the Director on :

(i)	the overall acceptability of any adverse environmental consequences that are likely to arise as a result of the proposed project;

(ii)	the conditions and requirements for the detailed design, construction and  operation of the proposed project to mitigate against adverse environmental consequences wherever practicable; and

(iii)	the acceptability of residual impacts after the proposed mitigation measures are implemented.

2.	OBJECTIVES OF THE EIA STUDY

2.1	The objectives of the EIA study are as follows:

(i)	to describe the proposed project and associated works together with the requirements for carrying out the proposed project;

(ii)	to identify and describe the elements of the community and environment likely to be affected by the proposed project and/or likely to cause adverse impacts to the proposed project, including both the natural and man-made environment;

(iii)	to identify and quantify emission sources and determine the significance of impacts on sensitive receivers and potential affected uses;

(iv)	to propose the provision of infrastructure or mitigation measures so as to minimize pollution, environmental disturbance and nuisance during construction and operation of the project;

(v)	to identify, predict and evaluate the residual (i.e. after practicable mitigation) environmental impacts and the cumulative effects expected to arise during the construction and operation phases of the project in relation to the sensitive receivers and potential affected uses;

(vi)	to identify, assesses and specify methods, measures and standards, to be included in the detailed design, construction and operation of the project which are necessary to mitigate these environmental impacts and reducing them to acceptable levels;

(vii)	to investigate the extent of side-effects of proposed mitigation measures that may lead to other forms of impacts;

(viii)	to identify  constraints associated with the mitigation measures recommended in the EIA study;

(ix)	to design and specify the environmental monitoring and audit requirements, if required,  to ensure the implementation and the effectiveness of the environmental protection and pollution control measures adopted.

3.	DETAILED REQUIREMENTS OF THE EIA STUDY

3.1	The Purpose

The purpose of this study brief is to scope the key issues of the EIA study.  The Applicant has to demonstrate in the EIA report that the criteria in the relevant sections of the Technical Memorandum on the Environmental Impact Assessment Process of the Environmental Impact Assessment Ordinance (thereafter referred to as the TM), are fully complied with.

3.2	The Scope

The scope of this EIA study covers the proposed project mentioned in section 1.2 above.

3.3	Technical Requirements

The Applicant shall conduct the EIA study to address all environmental aspects of the activities as described in the scope as set out above.  The EIA study shall include the following technical requirements on specific impacts :

3.3.1	Air Quality Impact

3.3.1.1	The assessment area for air quality impact shall generally be defined by a distance of 500m from the boundary of the project area(s).

3.3.1.2	For construction impacts, the Applicant shall follow the requirements of the Air Pollution Control (Construction Dust) Regulation in dust control and, subject to Section 4 below, shall initiate an audit and monitoring program during the construction stage to ensure construction dust impacts are controlled within the relevant standards as stipulated in Annex 4 of the TM.

3.3.1.3	For operational impacts, the air quality assessment shall address the following :

(i)	Analysis of operational activities and its characteristics.

(ii)	Presentation of background air quality in the study area for the purpose of evaluating the cumulative air quality impacts of the operational activities.

(iii)	Identification and description of representative existing air sensitive receivers (ASRs) and planned/committed air sensitive uses that would likely be affected by the air emissions of the operational activities. The locations shall be agreed with the Director and a map showing locations of all identified ASRs shall also be given.

(iv)	Identification of emission characteristics and provision of emission inventory of the air pollution sources.

(v)	Description of the assessment method and the associated assumptions, validity of the method and limits of application.  The methodology used shall be agreed with the Director before commencement of the EIA study.

(vi)	Assessment and evaluation of the net and cumulative air quality impacts of the air emissions at the identified ASRs. (Quantitative whenever applicable for air pollutants established with Air Quality Objectives)

(vii)	Presentation of the predicted residual air quality impacts (both unmitigated and mitigated) in the form of summary tables and pollution contours, for comparison with relevant air quality standards and the examination of the land use implications of these impacts.

(viii)	Proposals of appropriate mitigation measures to reduce the cumulative air pollution impacts to established standards, and to minimize any potential nuisance from the operation, such as engine testing and painting work.

(ix)	Submission of a copy of all input and output file(s) of the model run(s) in electronic format to the Director.

3.3.2	Noise Impact

3.3.2.1	The Applicant shall follow the criteria and guidelines for evaluating and assessing noise impact as stated in Annexes 5 and 13 of the TM, respectively.

3.3.2.2	The noise impact assessment shall include the following :

(i)	Determination of Assessment Area

The area for the noise impact assessment shall include all areas within 300m, in general, from the project boundary.  Subject to the agreement of  the Director, the assessment area could be reduced accordingly if the first layer of noise sensitive receivers, closer than 300m from the project boundary, provides acoustic shielding to those receivers at further distance behind.

(ii)	Provision of Background Information and Existing Noise Levels

The Applicant shall provide all  background information relevant to the project, e.g. relevant previous or current studies.  Unless involved in the planning standards, e.g. those for planning of fixed noise sources, no existing noise levels are particularly required.

(iii)	Identification of Noise Sensitive Receivers

(a)	The Applicant shall refer to Annex 13 of the TM when identifying the noise sensitive receivers (NSRs).  The NSRs shall include all existing NSRs and all planned/committed noise sensitive developments and uses earmarked on the relevant Outline Zoning Plans, Outline Development Plans and Layout Plans.

(b)	The Applicant shall select assessment points to represent all identified NSRs for carrying out quantitative noise assessment described below.  The assessment points shall be agreed with the Director prior to the quantitative noise assessment.  A map showing the location and description such as name of building, use, and  floors of each and every selected assessment point shall be given.

(iv)	Provision of an Emission Inventory of the Noise Sources

The Applicant shall provide an inventory of noise sources (e.g. construction equipment for construction noise assessment; fixed plant equipment, as appropriate, for operational noise assessment).  Confirmation of the validity of the inventory shall be obtained from the relevant government departments/authorities.

(v)	Construction Noise Assessment

(a)	The Applicant shall carry out assessment of noise impact from construction (excluding percussive piling) of the project during day time, i.e. 7 a.m. to 7 p.m., on weekdays other than general holidays in accordance with the methodology stipulated in paragraphs 5.3. and 5.4 of Annex 13 of the TM.  The criteria in Table 1B of Annex 5 of the TM shall be adopted in the assessment.

(b)	To minimize the construction noise impact, alternative construction methods to replace percussive piling shall be proposed as far as practicable.

(c)	If the unmitigated construction noise levels are found exceeding the relevant criteria, the Applicant shall propose practicable direct mitigation measures (including  movable barriers, enclosures, quieter alternative methods, re-scheduling and restricting hours of operation of noisy task) to minimize the impact.  If the mitigated noise levels still exceed the relevant criteria, the duration of the noise exceedance shall be given.

(d)	In case the applicant would like to evaluate whether construction works in restricted hours as defined under the Noise Control Ordinance (NCO) are feasible or not in the context of programming construction works, reference should be made to the relevant technical memoranda issued under the NCO.  Regardless of the results of construction noise impact assessment for restricted hours, the Noise Control Authority will consider a well-justified Construction Noise Permit (CNP) application, once filed, based on the NCO, the relevant technical memoranda issued under the NCO, and the contemporary conditions/situations of adjoining land uses and any previous complaints against construction activities at the site before making his decision in granting a CNP.  This aspect should be explicitly stated in the noise chapter and the conclusions and recommendations chapter in the EIA report.

(vi)	Operational Noise Assessment

(a) 	Fixed Noise Sources

(a1)	Assessment of Fixed Source Noise Levels

The Applicant shall calculate the expected noise using standard acoustics principles.  Calculations for the expected noise shall be based on assumed plant inventories and utilization schedule for the worst case scenario. The Applicant shall calculate the noise levels taking into account of correction of tonality, impulsiveness and intermittency in accordance with the Technical Memorandum for the Assessment of Noise from Places other than Domestic Premises, Public Places or Construction Sites.

(a2)	Presentation of Noise Levels

The Applicant shall present the existing and future noise levels in Leq (30 min) at the NSRs at various representative floor levels (in m P.D.) on tables and plans of suitable scale.

A quantitative assessment at the NSRs for the proposed fixed noise source(s) shall be carried out and compared against the criteria set out in Table 1A of Annex 5 of the TM.

(a3)	Proposals for Noise Mitigation Measures

The Applicant shall propose direct technical remedies within the project limits in all situations where the predicted noise level exceeds  the criteria set out  in Table 1A of Annex 5 of the TM to protect the affected NSRs.

(b)	Off-site Traffic Noise

As stated in the Project Profile (No. PP-050/1999), there will be potential off-site traffic noise impacts generated from buses leaving and returning to the proposed bus depot, in particular during early morning and night time.  Therefore, the Applicant shall evaluate such noise impacts in view of the noise sensitive receivers in the vicinity, and recommend suitable routings/mitigation measures to alleviate the traffic noise.

3.3.3	Waste Management Implications

3.3.3.1	The Applicant shall follow the criteria and guidelines for evaluating and assessing waste management implications as stated in Annexes 7 and  15 of the TM, respectively.

3.3.3.2	The assessment of waste management implications shall cover the following:

(i)	Analysis of Activities and Waste Generation

The Applicant shall identify the quantity, quality and timing of the waste arising as a result of the construction and operation activities, based on the sequence and duration of these activities.

(ii)	Proposal for Waste Management

(a)	Prior to considering the disposal options for various types of wastes, opportunities for reducing waste generation shall be fully evaluated.

(b)	Having been taken into account all the opportunities for reducing waste generation, the types and quantities of the wastes required to be disposed of as a consequence shall be estimated and the disposal options for each type of waste described in detail. The disposal meth