Company Information of Hong Kong Green Electroplating Company (HKGEC)

| Company Name | Hong Kong Green Electroplating Company (HKGEC) |
| --- | --- |
| Business Nature | Electroplating Nickel, silver, gold, palladium-nickel plating (rack plating) |
| Products | Electroplating for watch cases and belts |
| Major Markets | Local, China and Asia |
| Manufacturing Processes | Workpieces racking ( degreasing ( rinsing ( electro-degreasing ( rinsing ( acid dipping ( rinsing ( copper plating ( rinsing ( nickel plating ( rinsing ( silver / gold / palladium-nickel plating ( rinsing ( drying ( packing ( delivery |
| Address Office and Plant Locations | Blk B, 3/F, Vigor Industry Bldg, 49-53 Ta Chuen Ping Street Kwai Chung, NT Hong Kong |
| Factory Areas | 400 m2 |
| No. of Employees | 20 |
| Main Facilities / Equipment | Rack plating lines with tanks and associated equipment D.I. water generating system Wastewater treatment plant Ventilation system Oven |
| Surrounding Environment | Upper floors in a multi-storey industrial building located at Kwai Chung industrial area. Neighbor factories on the same floor are trading companies and a printing company. |
| Potential Environmental Impacts from the Operations | Wastewater discharge from degreasing, electroplating and rinsing processes. Wastewater is discharged to public sewer of the Victoria Harbor Water Control Zone. Solid wastes include general refuse, paper waste from office, packaging bags and rejected products. Chemical wastes from spent plating baths, sludge and chemical containers. Acid / alkaline / metal mists from electroplating baths Significant use of electricity, water and chemical for production processes |
| Special Client’s Environmental Requirements | Nil |

Disclaimer : The information provided in this practical example is purely hypothetical and intended to illustrate the development and implementation of ISO 14001 EMS.  Users will need to ensure that the information they insert is appropriate for their own situation.

HKGEC – Site Layout Plan

Process flow

Major Chemicals Used                       Process Step                      Waste Stream

Workpieces racking

Degreasing

Degreasing agent 
             Spent bath

(chemical waste)

Rinsing

Wastewater

Electro-degreasing

Wastewater

Rinsing

Wastewater

Acid Dipping

Dilute HCl
              Spent bath                                                                   					  (chemical waste)

Rinsing

Wastewater

Copper Plating

CuSO4
             Spent bath sludge 
Copper anode			(chemical waste)
Sulphuric acid

Rinsing

Wastewater

Ni Plating

NiCl, NiSO
             Spent bath sludge

Boric acid								  (chemical waste)

Rinsing

Wastewater

Palladium-nickel Plating

Gold Plating

Silver Plating

Rinsing

Wastewater

Drying

Products                        Packaging & Store

Delivery

HKGEC – Location Map in Hong Kong

(Blk B, 3/F, Vigor Industry Building, 49-53 Ta Chuen Ping Street, Kwai Chung)

# Text boxes

Drain

(Sampling point)

Wastewater Treatment Plant

Racking Area

## Silver Plating

## Degreasing

## Gold Plating

## Palladium-nickel Plating

Office

Office

## Office

## Nickel Plating

Store

# EXIT