Hong Kong Green Electroplating Company

Environmental Instruction Air Pollution Control (EI-04)

Revision No. : 1

Date : 01 – 01 – 2006

| Prepared by : | CC Wong |
| --- | --- |
|  | (EMR) |
| Approved by : | PH Lau |
|  | (General Manager) |

###### Revision History

| Revision Date | Description | Sections Affected | Revised By | Approved By |
| --- | --- | --- | --- | --- |
| 01-01-2006 | First issue | - - | - - | PH Lau |

- Purpose

This instruction outlines the practices to be adopted for the control of air emissions to minimise air pollution impacts and to comply with legal and other requirements.

- Scope

This instruction is applicable to the site activities, which have the potential to cause air pollution, and includes best practice procedures for the following:

- Emission of VOC and chemical fume from plating baths (e.g. during degreasing process);

- Maintenance / control over applicable activities and operations which generate airborne pollutants;

- Control of Chlorofluorocarbon (CFC) (e.g. refrigerants in air-conditioning units and CFC fire extinguishers).

- Procedure

  - Best Practices for Air Pollution

    - Emission of VOC and chemical fume from plating baths

- Ensure clean and clear ventilation points at the working areas.

- Ensure plating baths and degreasing baths are covered by lids when idle of operations, in order to reduce leakage of chemical fume to surroundings.

- Perform regular checking that ensure the setting of temperature for degreasing and plating baths are corrected, thus the baths should not generate too much chemical fume.

- If the plating baths are under maintenance / idle of operation, then all plating baths should be operated as ‘Switch Off / Stand-by’ mode, that ensure no chemical fume to be generated.

    - Maintenance / control over applicable activities and operations which generate airborne pollutants

- Ensure sufficient ventilation in indoor area especially rooms for chemicals usage and storage.

- Ensure that the air treatment equipments (e.g. air scrubbers, filtering system) function properly through regular inspection and maintenance.

    - Management of CFC

- Switch to air-conditioning units that use non-scheduled refrigerants during replacement.

- Switch to non-CFC fire extinguisher if applicable.

- Communicate with maintenance contractors for carrying out maintenance and repair of air-conditioning systems to ensure they work in accordance with requirements stipulated in the Ozone Layer Protection (Controlled Refrigerants) Regulations

- Monitoring and Checking

The Plant Manager or his / her delegate shall :

- ensure that plating baths are operated and maintained in satisfactory conditions;

- ensure the practices specified in this procedure are followed by staff and contractors.

- ensure the effective maintenance of plant and equipment through visual inspection and records review

- perform quarterly monitoring on the quality of indoor air.

- where nonconformity are identified corrective action measures are defined and implemented in accordance with EP-07 Enquiry / Complaint / Nonconformity Handling

- Records

| Record Description | Record Location/ Retention Responsibility | Minimum Retention Time |
| --- | --- | --- |
| Maintenance schedules / records for plant, equipment and vehicles (Refer to relevant subcontractors for plant, equipment and vehicles maintenance record) | Plant Manager | 3 years |
| Visual Inspection Records (Refer EF-EP07-01 if found any nonconformity) | Plant Manager | 3 years |

- Appendix

Nil.