HONG KONG GREEN ELECTRONIC ASSEMBLY COMPANY

Environmental Instruction Waste Management (EI-03)

Revision No. : 1

Date : 01 – 01 – 2006

| Prepared by : | Chan Fat |
| --- | --- |
|  | (EMR) |
| Approved by : | Wong Ming |
|  | (General Manager) |

###### Revision History

| Revision Date | Description | Sections Affected | Revised By | Approved By |
| --- | --- | --- | --- | --- |
| 01-01-2006 | First issue | - - | - - | Wong Ming |

- Purpose

This instruction outlines the practices to be adopted for waste management and to comply with legal and other requirements.

- Scope

This instruction is applicable to all activities and operations at HKGEAC which generates wastes and includes the best practice procedures for managing:

- Solid Waste, including:

  - General refuse from office activities

  - Stationery and office equipment (toner cartridges for printers, copiers, fax machines etc.)

  - Paper wastes

  - Recyclable waste (paper, plastic, aluminum cans, etc.)

  - Fluorescent lamps and batteries

  - Packaging materials (keep bubble wrap, plastic bags, etc. in good conditions for reuse; dispose only when material is deteriorated)

  - Rejected / damaged products (return to suppliers)

- Chemical Wastes, including:

  - Chlorine containing solvents

  - Empty chemical containers

- Procedure

  - Application for permits/licences

The EMR shall ensure that:

- a chemical waste producer licence is obtained for the company, and that the licence covers all the types of chemical waste produced by the company.

  - Practices for Waste Management

    - General Waste Management

- Segregation

  - Segregate the following solid wastes for disposal or recycling:

- Non-recyclable solid wastes (general refuse)

- Paper wastes (do not place non-recyclable paper including carbon paper, plastic laminated paper, glossy paper and contaminated papers in the recycle paper container)

- Packaging wastes (plastic, cartons)

- Wooden pallets for recycling

- Metal wastes for recycling (e.g. tin, lead, cadmium from soldering)

- Food waste

- Bulky items (e.g. furniture, machinery)

  - Clearly labelled containers must be located for the initial collection of these wastes as near as conveniently possible to the point of generation.

  - A designated member of staff (usually cleaning staff / contractor) should be assigned to collect the wastes and transfer them to the bulk waste storage area regularly.

- Storage

The following practices should be followed for the storage of solid wastes:

  - Segregate chemical waste and general waste in accordance with the allowable waste types listed on the containers.

  - Store all waste containers in dedicated storage areas.

  - Put lids/covers on all containers stored outside.

  - Label all waste containers and waste storage areas.

  - Store all waste containers on sealed ground to avoid land contamination

  - Make sure waste containers are collected when they are full.

  - Use containers that are strong enough to protect waste from wind, rain, scavengers and vandals.

The following practices should be avoided for the storage of solid wastes:

- The use of rusty, broken or leaky containers for the storage of solid waste

- Allowing waste to lie around that can be blown off site resulting in litter.

- Allow rainwater to enter waste containers where leachate may arise and contaminate surface waters.

- Disposal of Waste

When containers are observed to be full, a designated member of staff should arrange for a collection to be made by the waste disposal contractor.

    - Chemical Wastes

- Register with Environmental Protection Department (EPD) as Chemical Waste Producer and apply for a revision if the types of chemical waste to be disposed of change.

- Appoint licensed collector(s) (from EPD’s list of approved registered chemical waste collectors) to collect and dispose of chemical wastes

- Maintain records (trip tickets) of chemical wastes generated / collected.

- Adopt alternative working practices / processes to eliminate / reduce / generate less toxic chemical wastes

- Adopt storage, handling, transportation and disposal practices in accordance to the EPD publication “Code of Practice on the Packaging. Labelling and Storage of Chemical Wastes”:

- Provide appropriate wastes containers for each type of chemical waste generated on site. (Use container with capacity less than 450 litre unless specification approved by EPD.)

- Ensure that containers are in good condition, closed/ sealed.

- Put chemical waste labels with the appropriate information (in Chinese and English) on chemical waste containers

- maintain waste containers upright to minimise spillage/leakage.

- Designate separate storage facilities for incompatible chemical waste, and provide these areas with prominent signage, lock, etc.

- Provide secondary containment (e.g. drip trays or impermeable floor and bunding) and adequate ventilation for storage areas. (Capacity of the secondary containment should be able to accommodate 110% of the volume of the largest container or 20% of the total volume of waste stored, whichever is greatest.)

- Provide storage area with impermeable floor and bunding, and adequate ventilation.

- Provide storage facilities for vehicle batteries and/or battery acids

- Monitoring and Checking

The EMR shall ensure that:

- waste facilities specified in this EI are provided adequately and operated in satisfactory conditions; and

- waste management practices specified in this EI are followed by staff and contractors.

The Production Manager or his / her delegate shall:

- Check weekly if practices in Section 3.2 are correctly and fully implemented by random visual inspection, and note down the observation in the inspection checklist.

- When nonconformity are identified corrective action measures are defined and implemented in accordance with EP-07 Enquiry / Complaint / Nonconformity Handling.

- Records

| Record Description | Record Location/ Retention Responsibility | Minimum Retention Time |
| --- | --- | --- |
| Lists of chemicals wastes and storage locations (Refer to Production Manager) | Production Manager / EMR | Two previous versions |
| Information on waste collection company and frequency of collection locations (Refer to individual trip-ticket records and general waste collection records from subcontractor) | Production Manager / EMR | 3 years |
| MSDS for all chemicals and DGs (Refer to Production Manager) | Production Manager | 3 years |
| Trip Tickets (Refer to Production Manager) | Production Manager | 3 years |
| Visual Inspection Records (Refer to EF-EP07-01 if found any nonconformity item) | Production Manager / EMR | 3 years |

- Appendix

Nil.