(ACE-EIA Paper 15/2001)

# For information

Improvement to Tung Chung Road between Lung Tseng Tau and Cheung Sha

Advisory Council on the Environment-EIA Subcommittee Meeting on 5 November 2001

Purpose

This paper is to brief members of the ACE EIA Subcommittee of the current progress of the project and to seek their initial comments on the preferred road alignment of the project and the proposed future usage of the obsolete sections of Tung Chung Road. Members' comments will be considered in the EIA study and will not pre-empt the statutory EIA process.

Background

2.	In November 2000, the Director of Environmental Protection confirmed that the EIA Report of the proposed Lantau North-South Road link between Mui Wo and Tai Ho Wan could not meet the requirements of the Technical Memorandum of the EIA Ordinance and the study brief. After reviewing all possible alternative solutions, we considered that improvement to Tung Chung Road would be the most promising solution. At the ACE meeting on 27 February 2001, we briefed the ACE members of our proposal to improve Tung Chung Road to a rural 2 lane road with less than 15% gradients. We subsequently appointed consultants on 18 April 2001 to carry out an investigation study and preliminary design of the project.

Current Progress

3.	The investigation study of the project, including environmental impact assessment, traffic impact assessment, geotechnical assessment and drainage impact assessment, is in progress. The wet season ecological survey of the study area has been completed and an initial ecological impact assessment of the study area has been carried out. The dry season ecological survey is being carried out and will be completed in January 2002.

4.	Under the consultancy agreement, the consultant is required to refine the preliminary road alignment of the project by studying possible alternative alignment options within a broad corridor along Tung Chung Road and to recommend a preferred alignment option. The consultant has completed studying the possible alignment options and has recommended a preferred alignment option.

Environmental Characteristics of the Broad Corridor along Tung Chung Road

5.	The broad corridor passes between the Lantau and Sunset Peaks and is dominated by grass, shrubland, plantation woodland and secondary woodland. Areas of native secondary woodland are present mainly to the west of the Tung Chung Stream and near the coastline at Cheung Sha Sheung Tsuen. The natural woodland, together with the shrubland, represent the habitats of the greatest ecological value. The existing Tung Chung Road is largely bordered by shrubland and plantation woodland. A habitat map of the corridor is in Annex A.

6.	The Tung Chung Stream in the northern section of the corridor has been identified as the second richest stream in Hong Kong for freshwater fish species and is fed by numerous steep upland watercourses, which have a high degree of naturalness. The stream is one of only two known sites in Hong Kong for the Beijiang Thick-lipped Barb, a species regarded as being of conservation concern. This species and nine others including the Philippine Neon Goby, were recorded in the Tung Chung Stream and its tributaries during the wet season survey by the consultants. Streams in the southern hinterland are affected by the WSD catchwater which results in many streams having little or no flow. However, surveys of some of the larger streams, including the main Cheung Sha Stream and the stream at Cheung Sha Sheung Tsuen, have found two fish species of conservation interest, the Black-headed Thick-lipped Goby and the Philippine Neon Goby. Besides fish, some species of birds, insects and amphibians which are of conservation interest, including the Romer’s Tree Frog, can be found in the study area.

Alignment Options

7.	The possible alignment options within the corridor are shown on the drawing in Annex B. From Lung Tseng Tau to Tai Tung Shan Service Reservoir, all alignment options follow the existing road. Between the reservoir and the crest at Pak Kung Au, the existing road gradients dictate that the road can only be improved by going off-line. Four off-line alignment options have been developed for this northern section of the route. Options N1 and N2 are overland routes with slightly different road curves and gradients. Options N3 and N4 involve short tunnels of about 600 metres and 700 metres long respectively under the crest.

8.	Between the crest and South Lantau Road, the existing road can only be improved by going off-line. Four off-line alignment options have been developed. Option S1 runs down along the hillside on the eastside of Cheung Sha Valley and connects with South Lantau Road near the YWCA youth camp near Cheung Sha Sheung Tsuen. Option S2A also runs down along the hillside on the eastside of Cheung Sha Valley but then loops back north of the catchwater and runs westwards and connects with South Lantau Road at Cheung Sha Beach. Option S2B was similar to Option S2A but connects with South Lantau Road at the existing junction of Tung Chung Road and South Lantau Road. Option S3 runs along the west side of Cheung Sha Valley, crosses the catchwater and loops back to connect with South Lantau Road between Cheung Sha Beach and Tong Fuk Beach.

Options Assessment

9.	The alignment options were assessed in two stages, comprising the northern and southern alignment options separately. All relevant factors, including environmental, engineering, land use, cost and programme, were taken into account in the assessment of the alignment options.

10.	While full details of the options assessment will be included in the EIA report, a summary of the assessment results is in Annex C and is briefly explained below.

11.	In respect of the northern alignment options, the assessment shows that overall and environmentally, the overland route Option N1 is the most preferable option. The main reasons are:

- N1 has the least amount of earthworks and cut slopes which minimizes the land requirements from the Country Park (5.2ha) and the impacts associated with air quality, noise, waste and landscape and visual;

- N1 has the least potential for construction phase runoff which could affect Tung Chung Stream and Cheung Sha Stream;

- N1 requires the least construction cost and shortest construction programme.

12.	The tunnel options N3 and N4 are not recommended for the following reasons:

- The northern tunnel portals and the southern tunnel portals are close to the tributaries of Tung Chung Stream and Cheung Sha Stream respectively. Potential for significant construction impacts on these streams associated with tunnel dewatering activities will be great.

- Amount of earthworks required will be greater (about 150,00m3 more) than that of N1 and hence will have greater potential for impacts associated with water quality, ecology, air quality, noise and waste.

- For traffic safety and tunnel maintenance reasons, the tunnel would need to be a twin tube tunnel with 2 lanes in each tube.

- Areas of Country Park affected by N3(5.25ha) and N4(4.4 ha) are similar to that of N1(5.15ha).

- The construction cost is about $800M more than that of N1.

- The construction period will be 12 months more than that of N1.

13.	In respect of the southern alignment options, the comparison shows that overall and environmentally, Option S1 is the most preferable option. The main reasons are:

- S1 has the best alignment geometry avoiding the need for the large loop-bends associated with the other options;

- At the junction of S1 and South Lantau Road, there is space for construction of a roundabout and a bus-to-bus interchange;

- S1 has the least landscape and visual impacts;

- S1 largely avoids the high value secondary woodland;

- S1 requires the least amount of earthworks and thus presents environmental advantages in terms of ecology, landscape and visual impacts, waste and water quality;

- S1 has the least land requirement from the Country Park (2.3ha).

14.	Overall and environmentally, Option N1S1 as shown on the drawing in Annex D is the preferred alignment option. The alignment may be slightly refined or adjusted at the design stage to improve the road geometry and gradient The estimated cost of the project, based on Option N1S1, is $900M.

Future Usage of Obsolete Sections of Tung Chung Road

15.	Upon completion of the new road, some sections of the existing Tung Chung Road, mainly in the southern section, will become obsolete. The consultant has investigated all possible usage of the obsolete sections and has recommended the following usage:

- as a temporary traffic diversion route in the event of temporary closure of the new road due to serious traffic accidents;

- as a walking trail; and

- as accommodation for the existing and planned utility services.

16.	Demolition of the obsolete sections and reinstating the areas back to the natural condition are not recommended mainly because of the following reasons:

- large amount of earthworks would be required, which would have potential environmental impacts on the Tung Chung Stream and Cheung Sha Stream;

- the slopes along the obsolete sections require vehicular access for maintenance;

- the obsolete sections have many existing utility services; and

- many utility undertakers have requested to lay new utility services in Tung Chung Road, which should best be placed in the obsolete sections rather than the new road.

Way Forward

17.	Our consultants are proceeding with the EIA of the project, which is expected to be completed by the end of February 2002. In the EIA Report, we will fully address the concerns on this project expressed by members of the ACE at the meeting on 27 February 2001. These concerns includes:

- mitigation measures and post-construction management of the mitigation measures;

- plans and actions to preserve organisms in the streams near the alignment;

- means to reduce cutting slopes and landscape impact;

- future development in south Lantau;

- traffic control management on the new road;

- causes of traffic accidents on Tung Chung Road.

18.	To facilitate our completion of the EIA report, we welcome any initial comments which members may have on the preferred road alignment of the project and the proposed future usage of the obsolete sections of Tung Chung Road.

Highways Department

October 2001

# Assessment Summary – Northern Alignment Options

| Assessment Criteria | Option N1 Overland Route | Option N2 Overland Route | Option N3 Tunnel Route (Tunnel Length = 560m) | Option N4 Tunnel Route (Tunnel Length = 720m) |
| --- | --- | --- | --- | --- |
| Engineering Criteria |
| Alignment Geometry | Satisfactory geometry - relatively gentle bends with max gradient of 15%. | Satisfactory Geometry - more bends than N1 but length of 15% gradient slightly less than N1 | Better geometry - alignment gradient inside the tunnel at 3% | Better geometry - alignment gradient inside the tunnel at 3% |
| Geotechnical Constraints | Most favoured smallest amount of cutting slope > 8m high = 485m | Least favoured extensive cutting slope > 8m high = 805m | Least favoured mixed ground tunnelling required slope > 8m high = 355m (excluding slopes at tunnel portals) | Least favoured mixed ground tunnelling required slope > 8m high = 355m (excluding slopes at tunnel portals) |
| Highway Structures | Most favoured no. of bridges required = 4 total length = 155m | Least favoured no. of bridges required = 6 total length = 175m | Least favoured no. of bridges required = 6 total length = 185m | 2nd favoured no. of bridges required = 5 total length = 150m |
| Drainage Impacts | Stream crossings required = 6 | Stream crossings required = 5 | Stream crossings required = 6 | Stream crossings required = 4 |
| Impacts on Utilities | Cross 4 sets of overhead cables | Cross 5 sets of overhead cables | Cross 3 sets of overhead cables | Cross 3 sets of overhead cables |
| Environmental Criteria |
| Air Quality | Satisfactory | Satisfactory - higher impact during construction | Satisfactory - conc. of emissions at portals | Satisfactory - conc. of emissions at portals |
| Noise | Satisfactory | Satisfactory | Satisfactory | Satisfactory |
| Water Quality | Satisfactory | Less satisfactory - more earthworks and meanders closer to Tung Chung Stream | Least satisfactory - high suspended solid resulting from tunnel dewatering operation | Less satisfactory - high suspended solid resulting from tunnel dewatering operation |
| Construction Waste | Cut/fill surplus = 104,000m3 | Cut/fill surplus = 170,000m3 | Cut/fill surplus = 245,000m3 | Cut/fill surplus = 267,000m3 |
| Ecology | Least construction impact on Tung Chung Stream and Cheung Sha Stream. Habitat affected : secondary woodland = 0.5ha tall shrub = 1.2ha shrubland = 0.2ha plantation woodland = 3.1ha | Greater construction impact on Tung Chung Stream and Cheung Sha Stream than N1. Habitat affected : secondary woodland = 0.6ha tall shrub = 2.2ha shrubland = 0.2ha plantation woodland = 3.0ha | Greatest construction impact on Tung Chung Stream and Cheung Sha Stream. Habitat affected : secondary woodland = 1.1ha tall shrub = 1.8ha shrubland = 0.3ha plantation woodland = 2.1ha | Greatest construction impact on Tung Chung Stream and Cheung Sha Stream. Habitat affected : secondary woodland = 0.4ha tall shrub = 1.1ha shrubland = 0.1ha plantation woodland = 2.9ha |
| Landscape and Visual | 2nd favoured overland route, less cut slopes than N2 | 3rd favoured - overland route, more meanders and extensive cut slopes than N1 | Most favoured 560 m in tunnel, however, high cut slopes required at tunnel portals | Most favoured 720 m in tunnel, however, high cut slopes required at tunnel portals |
| Heritage | No impact | No impact | No impact | No impact |
| Hazard to Life | No impact (no potentially hazardous installation near the northern options) | No impact (no potentially hazardous installation near the northern options) | No impact (no potentially hazardous installation near the northern options) | No impact (no potentially hazardous installation near the northern options) |
| Land Use Criteria |
| Impacts on Country Park | Area affected = 5.15 ha | Area affected = 6.24 ha | Area affected = 5.25 ha | Area affected = 4.40 ha |
| Impacts on Private Land, etc | Minor | Minor | Minor | Minor |
| Impacts on Burial Ground | Minor | Minor | Minor | Minor |
| Costs and Programme Criteria |
| Capital Costs(excluding preliminary, contingencies, staff cost and ground investigation) | about $250M | about $290M | about $990M | about $1140M |
| Recurrent Costs | $ 2.4 M | $ 2.8 M | $ 23.8 M | $ 29.7 M |
| Time for Construction | Shortest | Longer (4 months longer than N1) | Longer (12 months longer than N1) | Longest(14 months longer than N1) |

# Assessment Summary – Southern Alignment Options

| Assessment Criteria | Option S1 Overland Route | Option S2A Overland Route | Option S2B Overland Route | Option S3 Overland Route |
| --- | --- | --- | --- | --- |
| Engineering Criteria |
| Alignment Geometry | Most favoured relatively smooth and straight | Less favoured - one big loop bend | Least favoured two big loop bends | Less favoured one big loop bend |
| Junction with South Lantau Road | Good connectivity to South Lantau Road. Sufficient space to construct roundabout and bus-to-bus interchange | Geometry of road junction not satisfactory. Insufficient space to construct roundabout and bus-to-bus interchange. Affect Cheung Sha Beach | Geometry of road junction not satisfactory. Insufficient space to construct roundabout and bus-to-bus interchange. | Geometry of road junction not satisfactory. Insufficient space to construct roundabout and bus-to-bus interchange. |
| Traffic Considerations | Most favoured - junction closer to Mui Wo the BTB at road junction | Less favoured - junction further from Mui Wo than S1 the BTB at road junction | Least favoured - junction further from Mui Wo than S1 the BTB not close to the road junction | Least favoured - junction further from Mui Wo than S1 the BTB not close to the road junction |
| Geotechnical Constraints | Most favoured less geotechnical works required slope > 8m high = 70m | Least favoured tall cut slopes required slope > 8m high = 210m | Least favoured tall cut slopes required slope > 8m high = 370m | Least favoured tall cut slopes required slope > 8m high = 410m |
| Highway Structures | Most favoured no. of bridges required = 9 total length = 460m | Less favoured no. of bridges required = 11 total length = 475m | Least favoured no. of bridges required = 13 total length = 630m | Least favoured no. of bridges required = 10 total length = 515m |
| Drainage Impacts | Stream diversions required = 1 | Stream diversions required = 3 | Stream diversions required = 3 | Stream diversions required = 2 |
| Impacts on Utilities | Cross 1 set of overhead cable | Cross 4 sets of overhead cables | Cross 3 sets of overhead cables | Cross 1 set of overhead cable |
| Environmental Criteria |
| Air Quality | Satisfactory | Satisfactory | Satisfactory | Least satisfactory - close proximity to Tung Fuk |
| Noise | Satisfactory | Satisfactory | Satisfactory | Least satisfactory - close proximity to Tung Fuk |
| Water Quality | Most favoured - least earthworks and impact on water quality; - outfall pipe will not affect gazetted beach | Least favoured - more earthworks and impact on Cheung Sha Stream; - outfall pipe will affect Cheung Sha Beach | Least favoured more earthworks and impact on Cheung Sha Stream outfall pipe will affect Cheung Sha Beach | Least favoured - more earthworks and impact on Cheung Sha Stream; - outfall pipe will affect Tong Fuk Beach |
| Construction Waste | Cut/fill surplus = 13,500m3 | Cut/fill surplus = 65,400m3 | Cut/fill surplus = 82,700m3 | Cut/fill surplus = 148,900m3 |
| Ecology | Least construction impact on Cheung Sha Stream. Habitat affected: secondary woodland = 0.6ha tall shrub = 1.6ha shrubland = 0.5ha plantation woodland = 2.0ha | Greater construction impact on Cheung Sha Stream. Habitat affected: secondary woodland = 1.1ha tall shrub = 1.2ha shrubland = 1.7ha plantation woodland = 1.7ha | Greater construction impact on Cheung Sha Stream. Habitat affected: secondary woodland = 1.4ha tall shrub = 1.9ha shrubland = 2.2ha plantation woodland = 2.3ha | Greatest construction impact on Cheung Sha Stream. Habitat affected: secondary woodland = 2.9ha tall shrub = 3.4ha shrubland = 0.4ha plantation woodland = 1.8ha |
| Landscape and Visual | Most favoured least cut/fill slopes and elevated structures required; avoid the need to cross Cheung Sha Valley. | Less favoured more cut/fill slopes and elevated structures required than S1; 12.5 m high viaduct at the loop bend; - visual impact on residents of Cheung Sha; - visual impact on users of Cheung Sha beach. | Least favoured extensive cut/fill slopes required; more elevated structures required than S1; 12.5 m and 30m high viaducts at the two loop bends; visual impact on residents of Cheung Sha; - visual impact on users of Cheung Sha beach. | Least favoured extensive cut/fill slopes required; more elevated structures required than S1; 11.7 m high viaduct at the loop bend; visual impact on residents of Tong Fuk; - visual impact on users of Cheung Sha beach. |
| Heritage | No impact. | No impact. | No impact. | No impact. |
| Hazard to Life | Satisfactory - far away from Cheung Sha water treatment works | Least satisfactory - closer to Cheung Sha water treatment works | Least satisfactory - closer to Cheung Sha water treatment works | Satisfactory - not affected by the Cheung Sha water treatment works |
| Land Use Criteria |
| Impacts on Country Park | Area affected = 2.29 ha | Area affected = 3.60 ha | Area affected = 3.60 ha | Area affected = 5.09 ha |
| Impacts on Government/Private Land, etc | Some proposed sale sites planned for residential purpose affected | Gazetted beach slightly affected | Some GLA affected and gazetted beach slightly affected | Some GLA affected |
| Impacts on Burial Ground and Fung Shui | No burial ground affected | No burial ground affected | No burial ground affected | Burial Ground No 48 |
| Costs and Programme Criteria |
| Capital Costs (excluding preliminary, contingencies, staff cost and ground investigation) | about $170M | about $200M | about $260M | about $240M |
| Recurrent Costs | $ 1.0 M | $ 1.6 M | $ 2.0 M | $ 2.0 M |
| Time for Construction | Shortest | Longer than S1 | Longer than S1 | Longest |

# Text boxes

Annex C