Attachment 3

Summary of Pipeline Route Options 1 and 2

|  | Pipeline Route from Tuen Mun Area 38 |
| --- | --- |
| Factors | to AFRF at Sha Chau (Option 1) | to Airport (Option 2) |
| Physical Factors Length Length within Marine Park Volume of Dredging (cubic metres) Duration of Pipelaying Cost Estimate (HK$million) | ~4.8 km ~400 m ~360,000 ~50 days ~200 | ~11.2 km nil ~835,000 ~100 days ~400 |
| Potential Environmental Impacts |  |  |
| During Construction Indo-Pacific Humpbacked Dolphins Ecology Marine Archaeology Contaminated Mud Pits | Base Case Base Case Base Case No Disturbance | More than double that of the Base Case More than double that of the Base Case More than double that of the Base Case Potential Disturbance |
| During Operation Normal operations Maintenance dredging needed at Sha Chau? | No impact Yes | No impact (but barges would still need to visit the AFRF) Yes |
| Operational Aspects Method of replenishing fuel in pipeline Use of PAFF tanks for storage during emergency Affects operation of airport during construction? | Not required Yes No | Achieved by barges to Sha Chau every 6 weeks or so No Yes |
| Overall Preference | Preferred | Not preferred |